# Voice-over-MQTT — Performance & Capacity Calculations
Scope / assumptions (read first)
- Audio codec = Opus (typical for voice). Use the codec bitrate you choose (e.g., 12, 20, 32, 64 kbps).
- Frame duration = 20 ms (common). → 50 frames/second. You can change frame duration and recompute.
- Transport: audio frames are sent in MQTT PUBLISH messages (QoS 0 for audio). Broker forwards frames to subscribers.
- Each packet on the wire contains: Audio payload + MQTT overhead + RTP/UDP/IP overhead. Ethernet/PHY overhead is ignored (we use IP layer).
- Broker is forwarding (not transcoding), so each audio frame published by A to topic(s) is forwarded to B (one publish in → one publish out). For 1:1 calls broker handles 2 directions (A→B and B→A). For group calls multiply accordingly.
- Use conservative broker message throughput of 400,000 msgs/s and network link capacity examples (1 Gbps, 100 Mbps). Replace with measured values for your setup.

## 1. Symbols / variables
- R = codec bitrate in bits per second (bps). (e.g., 20 kbps → R = 20000 bps)
- F = frames per second = 1 / frame_duration (for 20 ms frames → F = 50 fps)
- P_payload_bytes = average audio payload size per frame (bytes) = R / 8 / F
- H_mqtt_bytes = average MQTT overhead per publish (topic length + fixed header + var length). Assume 20 bytes (adjustable).
- H_rtp_udp_ip_bytes = RTP + UDP + IP headers (12 + 8 + 20 = 40 bytes)
- S_packet_bytes = total packet size on wire per audio frame = P_payload_bytes + H_mqtt_bytes + H_rtp_udp_ip_bytes
- S_packet_bits = S_packet_bytes * 8 (bits)
- BW_per_direction_bps = S_packet_bits * F (bits per second per direction)
- BW_per_call_bps = 2 * BW_per_direction_bps (full-duplex call)
- Msgs_per_stream_per_sec = F (publish messages per second per direction)
- Msgs_per_call_per_sec = 2 * F (both directions)
- Broker_msgs_total_per_sec = N_calls * Msgs_per_call_per_sec (messages broker must handle per second for N_calls)
- Broker_bw_total_bps = N_calls * BW_per_call_bps (network bandwidth through broker)

## 2. Formulas (summary)
1. P_payload_bytes = R / 8 / F
2. S_packet_bytes = P_payload_bytes + H_mqtt_bytes + H_rtp_udp_ip_bytes
3. S_packet_bits = S_packet_bytes * 8
4. BW_per_direction_bps = S_packet_bits * F
5. BW_per_call_bps = 2 * BW_per_direction_bps
6. Msgs_per_call_per_sec = 2 * F
7. For a given N_calls:
  1. Broker_msgs_total_per_sec = N_calls * Msgs_per_call_per_sec
  2. Broker_bw_total_bps = N_calls * BW_per_call_bps
8. Limits:
  1. N_calls_network_limit = floor( Link_capacity_bps / BW_per_call_bps )
  2. N_calls_msgs_limit = floor( Broker_msg_capacity_msgs_per_sec / Msgs_per_call_per_sec )
  3. N_calls_max = min(N_calls_network_limit, N_calls_msgs_limit)

## 3. Default header assumptions (can be tuned)
- H_mqtt_bytes = 20 bytes — topic and MQTT encoding. If your topic name is long, increase this.
- H_rtp_udp_ip_bytes = 40 bytes (RTP 12 + UDP 8 + IPv4 20).
- Frame duration = 20 ms → F = 50 fps.

## 4. Worked examples (replace numbers as needed)
We'll compute for these codec bitrates: 12 kbps, 20 kbps, 32 kbps, 64 kbps. Use H_mqtt_bytes = 20, H_rtp_udp_ip_bytes = 40, F = 50.
### Step-by-step numeric method (example for R = 20 kbps)
1. R = 20,000 bps
2. P_payload_bytes = 20000 / 8 / 50 = 20000 / 400 = 50 bytes
3. S_packet_bytes = 50 + 20 + 40 = 110 bytes
4. S_packet_bits = 110 * 8 = 880 bits
5. BW_per_direction_bps = 880 * 50 = 44,000 bps = 44 kbps
6. BW_per_call_bps = 2 * 44,000 = 88,000 bps = 88 kbps
7. Msgs_per_call_per_sec = 2 * 50 = 100 msgs/s (broker needed to process 100 messages per call per second)
So for 20 kbps Opus with 20 ms frames, each full-duplex call uses ~88 kbps and 100 msgs/s (broker msg load).

### Table of results (H_mqtt=20, H_rtp_udp_ip=40, F=50)
Codec bitrate (kbps)	Payload bytes/frame	Packet bytes	Bits/packet	BW per direction (kbps)	BW per call (kbps)	Msgs per call (msgs/s)
12	30	30+20+40=90	720	720*50=36,000 → 36 kbps	72 kbps	100
20	50	110	880	44 kbps	88 kbps	100
32	80	140	1,120	56 kbps	112 kbps	100
64	160	220	1,760	88 kbps	176 kbps	100

Note: Msgs per call stays at 100 msgs/s for 20 ms frames (50 fps × 2 directions).

## 5. Broker capacity examples
Assume:
- Link capacity = 1 Gbps (1,000,000 kbps) OR 100 Mbps (100,000 kbps)
- Broker message capacity = 400,000 msgs/s (conservative).
  Compute both limits and take the minimum.
### Example A — R = 20 kbps, per-call BW = 88 kbps, msgs per call = 100 msgs/s
- N_calls_network_limit = floor(1,000,000 kbps / 88 kbps) ≈ 11,363 calls
- N_calls_msgs_limit = floor(400,000 msgs/s / 100 msgs/s) = 4,000 calls
- N_calls_max = min(11,363, 4,000) = 4,000 calls
So on 1 Gbps network and a broker limited to 400k msgs/s, broker msg throughput is the bottleneck => ~4,000 concurrent 20 kbps calls.
If link is 100 Mbps:
- N_calls_network_limit = floor(100,000 / 88) ≈ 1,136 calls
- N_calls_max = min(1,136, 4,000) = 1,136 calls → network is the bottleneck.
### Example B — R = 32 kbps (per-call BW = 112 kbps)
- 1 Gbps network: floor(1,000,000/112) ≈ 8,928; msg limit still 4,000 → 4,000 calls (broker-limited).
- 100 Mbps network: floor(100,000/112) ≈ 892 → 892 calls (network-limited).
### Example C — R = 64 kbps (per-call BW = 176 kbps)
- 1 Gbps: ~5681 vs msg limit 4,000 → 4,000 calls (broker-limited).
- 100 Mbps: ~568 → 568 calls.

## 6. More reliable calculation: include CPU/IO limits
Broker message capacity (400k msgs/s) is an estimate. Real capacity depends on:
- CPU cores and single-core speed (EMQX uses multi-core).
- Whether messages use TLS (costly) — TLS will reduce msgs/s. If TLS is used, reduce Broker_msg_capacity by ~30–60% depending on CPU. Example: TLS enabled → set Broker_msg_capacity = 160k msgs/s as conservative.
- Disk persistence (writing messages to disk) further reduces throughput.
So recalc with TLS: for 20 kbps example, if Broker_msg_capacity = 160,000 msgs/s:
- N_calls_msgs_limit = floor(160000 / 100) = 1,600 calls
- On 1 Gbps net, N_calls_max = min(11,363, 1,600) = 1,600 calls

## 7. Group calls and multicast considerations
For group calls (1 publisher → M subscribers), broker forwards each incoming frame to M subscribers, so broker handles Msgs_per_stream_in * (1 + M) messages per frame. This drastically lowers capacity. Example: 1→9 (10 participants total): per frame broker does 1 in + 9 out → 10 forwards → message load ×10. Always account for number of recipients.

## 8. Practical checklist to compute for your setup
1. Choose codec bitrate R (e.g., 20 kbps).
2. Choose frame duration (20 ms → F=50).
3. Measure/choose H_mqtt_bytes (topic length + MQTT fixed overhead). Start with 20 bytes.
4. Use formulas above to compute BW_per_call_bps and Msgs_per_call_per_sec.
5. Choose Link_capacity_bps (e.g., 1 Gbps) and choose Broker_msg_capacity_msgs_per_sec (measure or use conservative 400k msgs/s, reduce for TLS/persistence).
6. Compute N_calls_max = min( floor(Link_capacity / BW_per_call), floor(Broker_msg_capacity / Msgs_per_call) ).
7. For group calls, multiply Msgs per call by number of recipients when computing broker message load.

## 9. Example: Complete calculation for your report (copy-ready)
Scenario: Opus 20 kbps, 20 ms frames, MQTT overhead 20 bytes, RTP/UDP/IP = 40 bytes, Link = 1 Gbps, Broker capacity (no TLS) = 400k msgs/s.
1. Payload bytes/frame = 20000 / 8 / 50 = 50 bytes
2. Packet bytes = 50 + 20 + 40 = 110 bytes
3. Bits/packet = 110 * 8 = 880 bits
4. BW per direction = 880 * 50 = 44,000 bps = 44 kbps
5. BW per call (full duplex) = 88 kbps
6. Msgs per call = 2 * 50 = 100 msgs/s
7. Network limit = 1,000,000 kbps / 88 kbps = 11,363 calls
8. Broker limit = 400,000 msgs/s / 100 msgs/s = 4,000 calls
9. Max concurrent calls = min(11,363, 4,000) = 4,000 calls
If TLS used and reduces broker capacity to 160k msgs/s:
Broker limit = 160,000 / 100 = 1,600 calls → Max = 1,600 calls.

## 10. Recommendations & practical tuning
- Use QoS 0 for audio to minimize overhead and latency.
- Minimize topic length to reduce MQTT overhead. Use short topics for audio streams (e.g., /a/ID/audio).
- Prefer local/edge brokers for low latency and to reduce cross-region bandwidth.
- For large deployments, use EMQX clustering to increase both network throughput and messages/s capacity. Each new broker node roughly increases message capacity linearly.
- Monitor real system metrics (emqx ctl metrics, CPU, net) and run stress tests (mqtt-stresser) to derive real Broker_msg_capacity for your hardware.
- For group calls, consider selective forwarding (SFU) or mixing strategies to reduce broker load (e.g., mix on server to lower per-client bandwidth).