## Complete EMQX Setup and Verification Commands
This documentation includes commands used for managing the service, checking logs, verifying configuration, and testing both unsecured and secure MQTT functionality.
### 1. System Management and Troubleshooting
These commands manage the EMQX service and help diagnose startup errors.
Command	Purpose
sudo systemctl status emqx	Check Service Status: Shows if the EMQX service is active (running) or has failed.
sudo systemctl start emqx	Start Service: Starts the EMQX daemon.
sudo systemctl stop emqx	Stop Service: Halts the EMQX daemon.
sudo systemctl enable emqx	Enable Service: Configures EMQX to start automatically on system boot.
sudo journalctl -u emqx.service --since "1 minute ago"	Check System Logs: Retrieves recent error messages from the system journal when EMQX crashes early.
sudo /usr/bin/emqx console	Force Console Mode: Runs the EMQX broker directly in the terminal to print detailed, immediate crash logs and diagnostics.
sudo chown -R emqx:emqx /var/lib/emqx /var/log/emqx /etc/emqx	Fix Permissions: Corrects file ownership to the emqx user, resolving common startup failures.

### 2. Network and Port Verification
These commands confirm that the broker is listening on the network interfaces.
Command	Purpose
sudo netstat -tulnp | grep -E "1883|8083|18083|8883"	Verify Open Ports: Checks if 1883 ($\text{TCP}$), 8083 ($\text{WebSocket}$), 18083 ($\text{Dashboard}$), and 8883 ($\text{TLS}$) are in the LISTEN state.
ip a	Find Local IP Address: Displays network interface details to find the current local $\text{IP}$ ($\text{e.g.,}$ $\text{192.168.1.2}$ or $\text{10.154.0.20}$) for client connections.

### 3. MQTT Functional Testing (MQTTX CLI)
These commands use your $\text{MQTTX}$ client to confirm that both unsecured and secure communication channels are active. (Note: These commands use your final working $\text{IP}$ address, 192.168.1.2).
#### A. Unsecured Channel Test (Port 1883)
Command	Purpose
mqttx sub -t "test/unsecured" -h 192.168.1.2 -p 1883	Subscriber: Connects to the standard, unsecured $\text{MQTT}$ port (1883).
mqttx pub -t "test/unsecured" -m "Message via Port 1883 (Unsecured)" -h 192.168.1.2 -p 1883	Publisher: Sends a test message over the unsecured channel.

#### B. Secure Channel Test (Port 8883)
Command	Purpose
mqttx sub -t "test/secure" -h 192.168.1.2 -p 8883 --ssl	Secure Subscriber: Connects to the $\text{Secure}$ $\text{MQTT}$ port (8883) using the $\text{TLS}$ protocol.
mqttx pub -t "test/secure" -m "Message via Port 8883 (Secure)" -h 192.168.1.2 -p 8883 --ssl	Secure Publisher: Sends a message over the $\text{secure}$ $\text{channel}$.