# Documentation of MQTT Voice Simulation, Latency & Jitter Calculation
Author: Ahmed
Date: 2025-11-13
Project: MQTT-based Voice Transmission Simulation

## 1. Overview
This project simulates real-time voice communication over MQTT. It consists of:
- TX (Transmitter): Publishes simulated voice frames with timestamps, variable frame sizes, and network jitter.
- RX (Receiver): Subscribes to frames, calculates latency, jitter, packet loss, logs per-frame data, and produces a final report.
The goal is to study end-to-end latency, jitter, and packet loss in a controlled, realistic scenario.

## 2. TX (Transmitter) – Mechanism
Key Features:
1. Frame Generation
  1. Each frame is a simulated audio block (e.g., PCM 16-bit 16 kHz → ~320 bytes for 20 ms).
  2. Frame size is variable to mimic compressed speech (50–320 bytes).
  3. Each frame contains:
    packet = {
    "seq": seq, # sequence number
    "timestamp": time.time(), # TX timestamp for latency calculation
    "size_bytes": frame_size, # frame size
    "data": payload.hex() # simulated audio data
    }
2. Frame Rate
  1. frame_duration = 0.02 s → 50 frames/sec.
3. Simulated Network Effects
  1. Jitter: random delay added between frames (0–40 ms).
  2. Packet loss: random drops (2%) to simulate real-world packet loss.
4. MQTT Publishing
  1. QoS = 0 (at-most-once, UDP-like behavior).
  2. Topic = voice/test.
TX Code Snippet:
payload = os.urandom(frame_size)
packet = {
    "seq": seq,
    "timestamp": time.time(),
    "size_bytes": frame_size,
    "data": payload.hex()
}
client.publish(topic, json.dumps(packet), qos=0)
time.sleep(frame_duration + random.uniform(*jitter_range))
Mechanism Notes:
- Each frame carries its exact send time (timestamp).
- Jitter simulates network delay variability.
- Packet loss simulates network unreliability.

## 3. RX (Receiver) – Mechanism
RX Responsibilities:
1. Receive MQTT messages
  1. Subscribes to voice/test topic.
  2. QoS = 0 → may miss packets (matches TX behavior).
2. Per-frame Metrics Calculation
Metric	Calculation	Purpose
Latency	latency_ms = (rx_time - tx_timestamp) * 1000	Measures end-to-end delay per frame
Jitter	jitter_ms = abs((rx_time - last_rx_time)*1000 - 20)	Variation from ideal 20 ms frame interval
Packet loss	if seq > expected_seq: lost += seq - expected_seq	Detect dropped frames using sequence numbers
Frame size	frame_size from packet	Track payload distribution

1. Intermediate Stats
  1. Every N frames (e.g., 100), calculate:
    avg_lat = statistics.mean(latencies[-N:])
    avg_jit = statistics.mean(jitter_list[-N:])
  2. Prints average latency, jitter, and packet loss.
2. CSV Logging
  1. Logs every frame: sequence, timestamps, latency, jitter, size.
  2. Enables offline analysis and plotting.
RX Code Snippet:
latency_ms = (now - tx_time) * 1000
latencies.append(latency_ms)
if last_rx_time is not None:
    jitter_ms = abs((now - last_rx_time)*1000 - 20)
last_rx_time = now
jitter_list.append(jitter_ms)
if seq > expected_seq:
    lost_frames += seq - expected_seq
expected_seq = seq + 1

## 4. End-to-End Latency Components
For a single frame, total one-way latency is approximated by:
L_total = L_capture + L_encode + L_packetize + L_tx + L_network + L_broker_proc
        + L_jitter_buffer + L_decode + L_playout_offset
Where:
Component	Description	Typical Values
L_capture	Frame capture at TX	20–25 ms
L_encode	Audio encoding	3–5 ms
L_packetize	Prepare MQTT payload	0.5 ms
L_tx	Serialize and send MQTT packet	0.01 ms (LAN)
L_network	Network propagation	10–30 ms (LAN)
L_broker_proc	Broker message processing	0.5–1 ms
L_jitter_buffer	RX buffering for jitter	20 ms
L_decode	Audio decoding	3 ms
L_playout_offset	Synchronization	0–1 ms

RX Measurement:
- latency_ms = rx_time - tx_timestamp includes all of the above except L_playout_offset.
- Jitter is calculated based on variation in inter-frame arrival.

## 5. Jitter Definition and Effect
- Definition: Variation in inter-arrival times of consecutive frames.
- Effect: Requires RX jitter buffer to smooth playback.
- High jitter → larger buffer → increases perceived latency.
- Formula in code:
jitter_ms = abs((now - last_rx_time)*1000 - 20)

## 6. Packet Loss
- Detection: RX tracks sequence numbers (seq).
- Impact: Missed frames → audio gaps in playback.
- Code:
if seq > expected_seq:
    lost_frames += seq - expected_seq
expected_seq = seq + 1

## 7. Variable Frame Sizes
- TX sends frames of 50–320 bytes to mimic real speech compression.
- RX logs frame sizes for statistics.
Purpose:
Reflects how real codecs generate smaller frames during silence and larger frames during speech activity.

## 8. CSV Logging and Reporting
- CSV fields: seq, tx_timestamp, rx_timestamp, latency_ms, jitter_ms, frame_size_bytes
- Intermediate Report: Every 100 frames, RX prints:
  Avg Latency, Avg Jitter, Lost frames
- Final Report: After simulation ends:
  Total frames received, Total packets lost,
  Latency: min/avg/max,
  Jitter: min/avg/max,
  Frame size: min/avg/max

## 9. Recommendations for More Realistic Simulation
1. Variable Network Latency: Inject LAN/WAN delays (e.g., 10–100 ms).
2. Realistic Codec Frames: Adjust frame size distribution using actual codec output (Opus, G.711).
3. Jitter Buffer Tuning: Use 1–3 frames to balance latency vs packet loss.
4. TLS/Encryption: Add encrypt/decrypt delay for security overhead.
5. Dynamic Packet Loss: Simulate bursty packet loss instead of random independent drops.

## 10. Summary of Script Logic
TX:
1. Generate variable size frame every 20 ms.
2. Add random jitter 0–40 ms.
3. Publish frame to MQTT topic (qos=0).
4. Simulate packet loss (2%).
RX:
1. Subscribe to MQTT topic.
2. On message receive:
  1. Calculate latency = rx_time - tx_timestamp
  2. Calculate jitter = difference from 20 ms ideal frame interval
  3. Track packet loss using seq
  4. Log to CSV
3. Every 100 frames, print intermediate stats.
4. On exit, print final detailed report with all statistics.
End-to-end latency is dominated by:
- Frame capture & encoding
- Network propagation
- Jitter buffering
- Decoding

TX – Realistic Voice Frames with Variable Size
import paho.mqtt.client as mqtt
import json
import time
import os
import random

# --- Configuration ---
broker_address = "127.0.0.1"
broker_port = 1883
topic = "voice/test"
client_id = f"TX_{os.getpid()}"

frame_duration = 0.02 # 20 ms per frame
frame_min_size = 50 # compressed voice frame min size in bytes
frame_max_size = 320 # max size
total_frames = 2000
drop_rate = 0.02 # 2% packet loss
jitter_range = (0, 0.04) # network jitter in seconds

client = mqtt.Client(client_id=client_id)

def connect_broker():
    print(f"🔗 Connecting to broker {broker_address}:{broker_port} ...")
    client.connect(broker_address, broker_port, 60)
    print("✅ Connected — starting voice stream\n")

def send_voice_stream():
    for seq in range(total_frames):
        if random.random() < drop_rate:
        # simulate packet loss
        time.sleep(frame_duration)
        continue

        frame_size = random.randint(frame_min_size, frame_max_size)
        payload = os.urandom(frame_size)
        packet = {
        "seq": seq,
        "timestamp": time.time(),
        "size_bytes": frame_size,
        "data": payload.hex()
        }

        client.publish(topic, json.dumps(packet), qos=0)

        # Simulate capture + encode + network + random jitter
        capture_encode = 0.025 # 25 ms: capture + encode
        network_delay = random.uniform(0.01, 0.03) # 10–30 ms
        jitter = random.uniform(*jitter_range)
        time.sleep(frame_duration + capture_encode + network_delay + jitter)

        if seq % 100 == 0:
        print(f"🎙️ Sent frame #{seq} | Size: {frame_size} bytes | Total simulated delay: {capture_encode*1000+network_delay*1000+jitter*1000:.1f} ms")

    print("\n✅ Transmission complete.")
    client.disconnect()

if __name__ == "__main__":
    connect_broker()
    send_voice_stream()

RX – Realistic End-to-End Latency
import paho.mqtt.client as mqtt
import json
import time
import statistics
import csv
import atexit

# --- Configuration ---
broker_address = "127.0.0.1"
broker_port = 1883
topic = "voice/test"
client_id = f"RX_{int(time.time())}"
REPORT_INTERVAL = 100 # report every N frames

# --- Globals ---
received_frames = 0
lost_frames = 0
expected_seq = 0
last_rx_time = None
latencies = []
jitter_list = []
frame_sizes = []

# --- CSV Logging ---
csv_file = open("voice_latency_log.csv", "w", newline="")
csv_writer = csv.writer(csv_file)
csv_writer.writerow(["seq","tx_timestamp","rx_timestamp","latency_ms","jitter_ms","frame_size_bytes"])

# --- Final report ---
def print_final_stats():
    if received_frames == 0:
        print("No frames received.")
        return

    avg_latency = statistics.mean(latencies)
    min_latency = min(latencies)
    max_latency = max(latencies)

    avg_jitter = statistics.mean(jitter_list)
    min_jitter = min(jitter_list)
    max_jitter = max(jitter_list)

    avg_frame = statistics.mean(frame_sizes)
    min_frame = min(frame_sizes)
    max_frame = max(frame_sizes)

    print("\n=== Final Detailed Voice Latency Report ===")
    print(f"Total frames received : {received_frames}")
    print(f"Total packets lost : {lost_frames}")
    print(f"Latency (ms) : min={min_latency:.2f}, avg={avg_latency:.2f}, max={max_latency:.2f}")
    print(f"Jitter (ms) : min={min_jitter:.2f}, avg={avg_jitter:.2f}, max={max_jitter:.2f}")
    print(f"Frame size (bytes) : min={min_frame}, avg={avg_frame:.1f}, max={max_frame}")
    print("=========================================\n")
    csv_file.close()
    print("📄 CSV log saved as 'voice_latency_log.csv'")

atexit.register(print_final_stats)

# --- MQTT Callbacks ---
def on_connect(client, userdata, flags, rc):
    if rc == 0:
        print(f"✅ Connected to broker {broker_address}:{broker_port}")
        client.subscribe(topic, qos=0)
        print(f"📡 Listening for voice frames...")
    else:
        print(f"❌ Connection failed with code {rc}")

def on_message(client, userdata, msg):
    global received_frames, lost_frames, expected_seq, last_rx_time

    now = time.time()
    try:
        data = json.loads(msg.payload.decode())
        seq = data["seq"]
        tx_time = data["timestamp"]
        frame_size = data["size_bytes"]

        # Simulate decoding + jitter buffer at RX
        decode_delay = 0.003 # 3 ms
        jitter_buffer = 0.02 # 20 ms
        time.sleep(decode_delay + jitter_buffer)

        # End-to-end latency
        latency_ms = (time.time() - tx_time) * 1000
        latencies.append(latency_ms)
        frame_sizes.append(frame_size)

        # Jitter
        if last_rx_time is not None:
        jitter_ms = abs((time.time() - last_rx_time)*1000 - 20)
        else:
        jitter_ms = 0
        last_rx_time = time.time()
        jitter_list.append(jitter_ms)

        # Packet loss detection
        if seq > expected_seq:
        lost_frames += seq - expected_seq
        expected_seq = seq + 1

        received_frames += 1

        # CSV log
        csv_writer.writerow([seq, tx_time, time.time(), f"{latency_ms:.2f}", f"{jitter_ms:.2f}", frame_size])

        # Intermediate report
        if received_frames % REPORT_INTERVAL == 0:
        avg_lat = statistics.mean(latencies[-REPORT_INTERVAL:])
        avg_jit = statistics.mean(jitter_list[-REPORT_INTERVAL:])
        print(f"\n--- Stats after {received_frames} frames ---")
        print(f"Avg Latency: {avg_lat:.2f} ms | Avg Jitter: {avg_jit:.2f} ms | Lost frames: {lost_frames}")
        print("----------------------------------\n")

    except Exception as e:
        print(f"⚠️ Error parsing message: {e}")

# --- Main ---
client = mqtt.Client(client_id=client_id)
client.on_connect = on_connect
client.on_message = on_message

print(f"🔗 Connecting to broker {broker_address}:{broker_port}...")
client.connect(broker_address, broker_port, 60)
client.loop_forever()